## Slide 1: Structural Wing Model Reduction in Fluid-Structure Interactions
STUDENT:
Oriol CHANDRE VILA
TUTORS:
Joseph MORLIER and Sylvain DUBREUIL (ONERA)
Project of Innovation and Research (PIR)
Spring 2018
[Amsallem, International Journal for Numerical Methods in Engineering, 2014]

## Slide 2: Table of Contents
Introduction
Aim and Objectives
State of the Art: ROM
Results
Integration of ROM to Aeroelasticity
Future work
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA

## Slide 3
Introduction
Aeroelasticity
Coupling between aerodynamic forces, inertial forces and elastic forces.
Current issues due to models dimension. Why the ROM?
The calculations have a high cost in time and computational power.
Mean vorticity field
[Kutz et al., Chpt 9, SIAM, 2016]
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
[Kutz et al., Chpt 9, SIAM, 2016)

## Slide 4
Aim & Objectives
Aim
To study the use of Reduced Order Models (hereafter ROM) in order to lighten the computational requirement in fluid-structure problems simulations
Objectives
To study different ROM methodologies.
To apply ROM techniques to a simple problem.
To define a strategy for fluid-structure interactions problems.
Source [8]
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA

## Slide 5
State of the Art: ROM
Principal Component Analysis (PCA)
Widely used in the actuality.
Limitations:
  The results depend on the scaling variables.
  The applicability is limited by certain assumptions.
  No differentiation between classes.
Used in different disciplines:
  SVD in Algebra
  POD in Mechanical Engineering.
Possible correlated variables
(Observations)
Orthogonal Transformation
Values of linearly uncorrelated variables
(Principal Components)
SVD approach:
In Matlab:
[U,S,V] = svd(A)
[Ar] = U(:,1:k)*S(1:k,1:k)*V(:,1:k)’
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
[Kutz, Chpt 15, Oxford University Press, 2013]

## Slide 6
State of the Art: ROM
Dynamic Mode Decomposition (DMD)
DMD is not a ROM itself, it is more a strategy. However, it uses ROM (usually SVD) to perform a low-rank truncation of the data.
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
[Kutz, SIAM, 2016]
[Kutz, Chpt 20, Oxford University Press, 2013]
AIM:
To take advantage of the low dimensionality in the experimental data.
WHAT DOES DMD PROVIDE?
A decomposition of experimental data into a set of dynamic modes.
HOW DOES IT WORK?
DMD computes the eigenvalues and eigenvectors of the linear model.
ADVANTAGES:
No equations are needed.
The future state is known for all time.
WHEN DOES IT FAIL?
Data matrix is full rank
No suitable low dimensional structure.

## Slide 7
Fast ONLINE solution of a recurring problem.
PGD is a numerical method for solving boundary value problems.
Its biggest advantage is the ability to work in a Parameterized approach.
The vectors R(x), S(y), T(z),, Z(n) are robustly computed offline.
The vectors R(x), S(y), T(z), ⋯ , Z(n) are robustly computed offline.
Fast ONLINE solution of a recurring problem.
PGD is a numerical method for solving boundary value problems.
Its biggest advantage is the ability to work in a Parameterized approach.
State of the Art: ROM
Proper Generalized Decomposition (PGD)
PGD is not a ROM itself, it is more a strategy. However, it can use ROM to economize the vectors solutions R, S, T,, Z .
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
[Chinesta et al., Springer, 2014]

## Slide 8
State of the Art: ROM
Analysis of Performance of ROM
Galerkin Reduced Basis (G-RB) + POD or Greedy Algorithm.
The parametric dependence of the PDE solution is exploited.
PROBLEM: Steady heat conduction-convection problem.
Error bounds :
To compute the norm:
To compute the stability factor () with Interpolatory Radial Basis function.
To compute the error estimator:
High-fidelity model |  | Reduced-Order model | 
# FE dofs () | 44171 | # RB dofs | 29
Affine operator components () | 2 | Dofs reduction | 1520:1
Affine RHs components () | 6 | Offline CPU time | min
FE solution time | s | Online CPU time | 1 ms
High-fidelity model |  | Reduced-Order model | 
 | 44171 | # RB dofs | 29
 | 2 | Dofs reduction | 1520:1
 | 6 | Offline CPU time | 
FE solution time |  | Online CPU time | 1 ms
Table 2. Computational details for HF and RB models. [Quarteroni et al., Chpt 3, Springer, 2016]
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
[Quarteroni et al., Springer, 2016]
Figure 1. Comparison of the average error and bound error estimator computed on a set of 350 random values. [Quarteroni et al., Chpt 3, Springer, 2016]

## Slide 9
State of the Art: ROM
POD approach using:
Error estimator
Latin Hypercube Sampling (LHS)
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
Figure 2. First 55 singular values of the correlation matrix obtained by LHS. [Quarteroni et al., Chpt 6, Springer, 2016]
Figure 3. Convergence history of the greedy algorithm. [Quarteroni et al., Chpt 7, Springer, 2016]
Greedy algorithm critical aspects:
Use of
It is not necessarily faster than POD
Greedy algorithm + POD:
Error estimator
Latin Hypercube Sampling (LHS)
Potentially faster

## Slide 10
{█(𝒯(𝒙;𝝁)=𝒯_𝐷 (𝑦;𝑦 ̅ )@𝛻𝒯(𝒙;𝝁)⋅𝒏(𝒙)=0)┤
𝒯_𝐷 (𝑦,𝑡;𝑦 ̅ )={█(300@300+325(sin⁡(3⋅𝜋⋅|𝑦−𝑦 ̅ |)+1)^ @300)┤
𝑦 ̅∈[0,4;0,6]
Results
  Advection-Diffusion problem definition
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
[Amsallem, International Journal for Numerical Methods in Engineering, 2014]
if
if
if
BOUNDARY
CONDITIONS
Steady Advection-Diffusion
Steady Advection-Diffusion
𝒰⋅𝛻𝒯−𝜅⋅∆𝒯=0
;
𝒰=[■8(𝒰_1@𝒰_2 )]=[■8(𝒰_1@0)] ;〖 𝒰〗_1 𝜖 [0;0,5]
𝜅 𝜖 [0;0,025]
𝒙=(𝑥,𝑦)∈[0,1]×[0,1]

## Slide 11
Results
  Advection-Diffusion problem: POD
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
Algorithm Greedy POD
Select randomly a first sample:
Solve the HDM:
Build a corresponding ROB:
For i = 2 ,, s
  Solve:
  Solve the HDM:
  Build a ROB based on the samples
Time computing performance:
Solution accuracy:
[Amsallem, International Journal for Numerical Methods in Engineering, 2014]
V size:
3487 x 10 =
34870 terms

## Slide 12
Results
  Advection-Diffusion problem: PGD
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
5 coordinates:
Residual Minimization Technique for PGD
The search of a less intrusive method
A non-symmetry induced by the convection terms.
2 diffusion eq. + 2 advection eq.
AA = cell(5,4)
BB = cell(5,1)
RHS: Source terms
N_NT = cell(5,1)
Mass matrices
Dirichlet = cell(5,1)
Where to apply Dirichlet BC:
GG = cell(5,1)
A priori known terms, to enforce the Dirichlet BC
GG {2} =
Neumann BC
D1x(end,end) = 0;
D1y(1,1) = 0; D1y(end,end) = 0;
[Chinesta et al., Springer, 2014]

## Slide 13
Results
  Advection-Diffusion problem: PGD
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
OFFLINE
ONLINE
Loop | Stopping Criterion | Tolerance
Fixed point |  | 
PGD enrichment |  | 
Loop | Stopping Criterion | Tolerance
Fixed point |  | 
PGD enrichment |  | 
Computing time:
43min 25s
Computing time:
0,1 – 0,5 s
alph = ones(size(FF{1},2),1);
alpha = FF{3}(5,:) .* FF{4}(1,:) .* FF{5}(15,:) .* alph';
T = FF{2} * diag(alpha) * FF{1}';
!!!
FF size: 292500 terms

## Slide 14
Conclusions
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
PGD  a lot of cases of the same (normally expensive) problem are expected.
DMD  simulations in time domain. We need a film of snapshots to create the reduced model.
POD
PGD
The most interesting PGD’s approach is the Parametric PGD.
PGD allows to introduce Boundary Conditions as extra-coordinates of the problem.
The Stopping Criterion and Tolerance effectiveness should be evaluated for each problem.

## Slide 15
Future work
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA
Modification of the Stopping Criterion.
SUMMER INTERSHIP IN ONERA
Application of the strategy into OpenAeroStruct.
SUMMER INTERSHIP IN ONERA
Link to the GitHub Project

## Slide 16
References
[1] Kutz, J.N., Brunton, S.L., Brunton, B.W. and Proctor, J.L., "Dynamic Mode Decomposition: Data-Driven Modeling of Complex Systems", 1st ed., SIAM, Philadelphia, 2016.
[2] Kutz, J. N., "Data-Driven Modeling & Scientific Computation: Methods for Complex Systems & Big Data", 1st ed., Oxford University Press, Oxford, 2013.
[3] Chinesta, F., Keunings, R. and Leygue, A., "The Proper Generalized Decomposition for Advanced Numerical Simulations: A primer", 1st ed., Springer, 2014.
[4] Quarteroni, A., Manzoni, A. and Negri, F., "Reduced Basis Methods for Partial Differential Equations. An Introduction", Unitext, vol. 92. Springer, 2016.
[5] Amsallem, D., “An Adaptive and Efficient Greedy Procedure for the Optimal Training of Parametric Reduced-Order Models”, International Journal for Numerical Methods in Engineering, 2014.
[6] http://www.dlr.de/ae/en/desktopdefault.aspx/tabid-1596/
Structural Wing Model Reduction in Fluid-Structure Interactions | Oriol CHANDRE VILA